## Slide 1
c
Results
Related Works
Introduction
Practical Improvements of Soil Organic Carbon (SOC) Sensing with Machine Learning, Satellite and Ground Data
Dong-Yoon Kim1, Woo-Young Park2, Jin-Seong Kim3, Su-Min Oh4, Alfred Cueva5
1Department of Physics and Astronomy, 2Department of Environmental Engineering, 3College of Liberal Studies, 4Department of Economics, 5Department of Mechanical Engineering, Seoul National University,1 Gwanak-ro, Gwanak-gu, Seoul 08826, Republic of Korea
Importance of Soil Health and SOC
95% of our food comes from topsoil
[1] UNFAO, 2019
[3] Plant Sci, 2017
[2] Global Change Bio, 1997
Microbe biodiversity helps crop growth
Soil is the largest terrestrial carbon sink
Hand-held spectroradiometer
Hi-Res NG
Spectroradiometer
Increase in SOC
Optical Characteristic of SOC
Reading Spectral Reflectance to determine SOC
Spectroradiometer extremely expensive ~ $100,000
Common farmers cannot afford
Not a scalable solution
[12] Int. Soil & Water Cons. Res. 2020
Reflectance (%)
…
Discrete bands instead of continuous spectrum
Sentinel-2 with revisit time of 5 days Imaging entire Earth
[13] Remote Sens. 2021
Scalable solution as Sentinel-2 images over entire Earth surface and open-source
Not accurate enough with R2 = 0.57 between predicted and actual SOC
Increase in SOC
MSI
bands
Reflectance (%)
Reflectance (%)
Multi-Spectral Imagery (MSI)
Our Strategy
Approach 1 (Hybrid Remote Sensing)
Approach 2 (Full Remote Sensing)
SOC (%)
SWHC (%)
SOC ↑↑↑  Soil Water Holding Capacity (SWHC)↑↑↑
[14] Int. J. Ecol. Environ. Sci, 2009
H2O
+
+
Sand
Silt
Clay
MSI
SWHC
Soil Texture
ML regression model to accurately predict SOC level
Simple, Cheap  Anyone (farmers etc.) can test
Radar
Antenna
Sentinel-1 Synthetic Aperture Radar (SAR)
MSI
+
Surface
Soil Moisture (%)
BackscatterVV (dB)
B4 rain
Rain
Aft rain
Difference of Soil Moisture before and after rain can give us idea how well soil retains water
ML
Reg.
More accurate than just MSI
Global Issue of SOC degradation
Unsustainable farming
Inadequate fertilizer
Overgrazing etc.
By 2050, likely 90% of global topsoil will degrade
Farmer suicide rate ↑↑↑ (300,000 in India alone) due to harvest < debt
[7] UNCCD, 2020
[21] National Crime Records Bureau, 2021
[20] Sustainable Land Use Management, 2017
Wavelength (nm)
Hence SOC sensing/monitoring is important because
Soil degradation prevention
Food security monitoring
Enforce pro-soil policy
[22] Nature 601, 503-504 (2022)
But current method to measure SOC (Walkley-Black test) is too slow, uses dangerous chemicals
[11] Soil & Man., 2007
Need to cheaply monitor SOC at scale and at real-time
Trained only on Raw MSI Image (Resolution = 20m) |  |  | 
Models | SVM | PLSR | RF
Train R2 | 0.22 | 0.48 | 0.70
Test R2 | 0.21 | 0.30 | 0.52
MSI Image enhanced with Super-Resolution (Resolution = 10m) |  |  | 
Models | SVM | PLSR | RF
Train R2 | 0.57 | 0.38 | 0.69
Test R2 | 0.33 | 0.25 | 0.38
Test R2 = 0.74
Approach 2
(MSI + SAR  RF)
Test R2 = 0.83
Approach 1
(MSI + SWHC + ST  RF)
Test R2 = 0.52
Only MSI  RF
Similar results with previous works
60% Accuracy Increase
42% Accuracy Increase
Top 3 features have wavelengths 1610nm, 665nm, 740nm
Associated with SOC chemistry
SAR data has notable influence in prediction but less than expected due to influence of soil roughness
Random Forest (RF) model showed better accuracy than Support Vector Machine (SVM) & Partial Least-Squares Regression
Information loss in resolution enhancement as enhancement done based on only 4 bands out of 13 bands
Feature Importance (a.u.)
B2
B3
B4
B5
B6
B7
B8
B8A
B11
B12
Top 10 most important features for SOC prediction
Conclusion
Approach 1 is cheap and easy able to accurately determine farmer’s SOC:
Farmer measure ST and SWHC
Send data to operator
Add MSI data
SOC determined
Practical Implementation:
Approach 2 is less accurate than approach 1 but it is full-remote sensing  Robust means of global monitoring
MSI + SAR
Global Monitoring
Danger Area Detected
Check with Approach 1
Practical Implementation:
Detect & Prevent soil degradation  Improve agriculture
Monitor soil carbon sequestration  Help mitigate climate change
Only MSI
Top 4 features show predictive power of ST and SWHC
ST importance > SWHC importance
Approach 1
Approach 2
*DSM = Delta Soil Moisture